;Bee Cha
;Lab 10
;Implement a 16-bit ALU
;Perform the 1-bit ALU for each 16-bit
;Do different operation controled by the binv and op
;Output results

.586
.MODEL FLAT

INCLUDE io.h ; header file for input/output

.STACK 4096

.DATA

prompt1	BYTE	"Enter a, b, carry in, and op code", 0
a	DWORD	?
b	DWORD	?
binv	DWORD	?
op	DWORD	?
arg	BYTE	40 dup(?),0
temp	BYTE	4 dup(" "),0
temp2	BYTE	?
and_result	DWORD	?
or_result	DWORD	?
xor_result	DWORD	?
add_result	DWORD	?
cin_plus	DWORD	?
si_result	DWORD	?
carry	DWORD	?
result_str	BYTE	2 dup(" "), 0
outlbl	BYTE	"Result 1-Bit ALU", 0
label2	BYTE	"ai", 09h, "bi", 09h, "ci", 09h, "op", 09h, "Si", 09h, "Ci+1", 0dh, 0	;20 characters
outstr	BYTE	400 dup(?), 0

.CODE
_MainProc PROC

input	prompt1, arg, 40	;Get user input

lea	ebx, arg
lea	edx, temp
mov	ecx, 0

loop1:
cmp	BYTE ptr [ebx], 20h	;Compare if it's a blank space
je	done1
cmp	BYTE ptr [ebx], 00h	;Compare if it's a null space
je	done1
mov	AL, byte ptr [ebx]	;Otherwise get 1 byte from it
mov	[edx], AL	;And put it in temp string
inc	ecx
inc	edx
done1:
inc	ebx
cmp	ecx, 4
jl	loop1

;-----Convert each parameters in [EBX] into dword, ATOD-----;

lea	edx, temp
mov	AL, byte ptr [edx]
mov	temp2, AL
atod	temp2
mov	a, eax

inc	edx
mov	AL, byte ptr [edx]
mov	temp2, AL
atod	temp2
mov	b, eax

inc	edx
mov	AL, byte ptr [edx]
mov	temp2, AL
atod	temp2
mov	binv, eax

inc	edx
mov	AL, byte ptr [edx]
mov	temp2, AL
atod	temp2
mov	op, eax

;-----Now you have the corresponding arguments: a, b, binv, and op-----;

push	a
push	b
push	binv
push	op
push	and_result
push	or_result
push	xor_result
push	carry
call	test_proc
add	esp, 32

        mov eax, 0 ; exit with return code 0
        ret
_MainProc ENDP

test_proc	PROC

;---STACK---;
;	[ebp+36] = a
;	[ebp+32] = b
;	[ebp+28] = binv
;	[ebp+24] = op
;	[ebp+20] = and_result
;	[ebp+16] = or_result
;	[ebp+12] = xor_result
;	[ebp+8] = carry

push	ebp
mov	ebp, esp

push	[ebp+36]
push	[ebp+32]
call	AND_gate
mov	[ebp+20], eax	;and_result
call	OR_gate
mov	[ebp+16], eax	;or_result
call	XOR_gate
mov	[ebp+12], eax	;xor_result
add	esp, 8

push	xor_result
push	and_result
push	binv
call	full_adder
mov	[ebp+8], eax	;carry
add	esp, 12

pop	ebp
ret

test_proc	ENDP

;-----GATE PROCEDURES-----;

AND_gate	PROC

;-----AND_gate takes parameters a and b then it will AND the results back-----;
push	ebp
mov	ebp, esp

mov	eax, [ebp+12]
and	eax, [ebp+8]

pop	ebp
ret

AND_gate	ENDP

OR_gate	PROC

;-----OR_gate takes parameters a and b then it will OR the results back-----;
push	ebp
mov	ebp, esp

mov	eax, [ebp+12]
or	eax, [ebp+8]

pop	ebp
ret

OR_gate	ENDP

XOR_gate	PROC

push	ebp
mov	ebp, esp
mov	eax, [ebp+12]
xor	eax, [ebp+8]

pop	ebp
ret

XOR_gate	ENDP

full_adder	PROC

;-----Full Adder: Ai XOR Bi XOR cin-----;
;[ebp+8]	= binv
;[ebp+12]	= and_result
;[ebp+16]	= xor_result

push	ebp
mov	ebp, esp

;xor_result AND binv
;If subraction, AND gate will invert B
mov	eax, [ebp+16]	;xor_result
and	eax, [ebp+8]	;xor_result AND binv

;(xor_result AND binv) OR and_result
or	eax, [ebp+12]	;carry result

pop	ebp
ret

full_adder	ENDP

END ; end of source code

;Bee Cha
;Lab 10
;Implement a 16-bit ALU
;Perform the 1-bit ALU for each 16-bit
;Do different operation controled by the binv and op
;Output results

.586
.MODEL FLAT

INCLUDE io.h ; header file for input/output

.STACK 4096

.DATA

prompt1	BYTE	"Enter A: 16-bit binary", 0
prompt2	BYTE	"Enter B: 16-bit binary", 0
prompt3 BYTE	"Enter Control Signal: 3-bit binary", 0
a	BYTE	16 dup(?),0
b	BYTE	16 dup(?),0
binv	BYTE	?
op	BYTE	2 dup(?), 0
arg	BYTE	40 dup(?),0
and_result	DWORD	?
or_result	DWORD	?
xor_result	DWORD	?
add_result	DWORD	?

carry	DWORD	?
result_str	BYTE	2 dup(" "), 0
outlbl	BYTE	"Result 1-Bit ALU", 0
label2	BYTE	"ai", 09h, "bi", 09h, "ci", 09h, "op", 09h, "Si", 09h, "Ci+1", 0dh, 0	;20 characters
outstr	BYTE	400 dup(?), 0

.CODE
_MainProc PROC

input	prompt1, arg, 40	;Get A input
mov	ecx, 0
lea	ebx, arg
lea	edx, a

;-----Convert each bit into numeric value then move it to A-----;
loop1:
mov	AL, BYTE ptr [ebx]
sub	AL, 30h
mov	BYTE PTR [edx], AL

inc	edx
inc	ebx
inc	ecx

cmp	ecx, 16
jl	loop1

input	prompt2, arg, 40	;Get B input
mov	ecx, 0
lea	ebx, arg
lea	edx, b

;-----Convert each bit into numeric value then move it to B-----;
loop2:
mov	AL, BYTE ptr [ebx]
sub	AL, 30h
mov	BYTE PTR [edx], AL

inc	edx
inc	ebx
inc	ecx

cmp	ecx, 16
jl	loop2

input	prompt3, arg, 40	;Get control signal input
lea	ecx, arg
mov	AL, BYTE PTR [ecx]
sub	AL, 30h	;Convert Binv to numeric value

mov	binv, AL

inc	ecx
mov	AL, BYTE PTR [ecx]
sub	AL, 30h	;First OP bit

inc	ecx
mov	BL, BYTE PTR [ecx]
sub	BL, 30h	;Zeroth OP bit

mov	DL, 0
cmp	AL, 1
jne	skip1
add	DL, 2
skip1:
cmp	BL, 1
jne	skip2
add	DL, 1
skip2:
lea	ebx, op
mov	BYTE PTR [ebx], DL	;Stores corresponding OP code, 0 1 2

;-----Now you have the corresponding arguments: A, B, binv, and op-----;
;-----Perform 1-bit ALU operation on each bit-----;

lea	ecx, a
lea	edx, b
mov	eax, [ecx+15]
and	eax, [edx+15]

        mov eax, 0 ; exit with return code 0
        ret
_MainProc ENDP

test_proc	PROC

push	ebp
mov	ebp, esp

mov	eax, [ebp+8]
and	eax, [ebp+12]

pop	ebp
ret

test_proc	ENDP

one_bit	PROC

;---STACK---;
;	[ebp+8]	= address of binv
;	[ebp+12]	= address of op
;	[ebp+16]	= address of b
;	[ebp+20]	= address of a

;Compare OP code to determine what operation to do
;If OP = 1, then do subraction

mov	eax, 4

SUBTRACTION:

push	ebp
mov	ebp, esp

pop	ebp
ret

one_bit	ENDP

;-----GATE PROCEDURES-----;

AND_gate	PROC

;-----AND_gate takes parameters a and b then it will AND the results back-----;
push	ebp
mov	ebp, esp

mov	eax, [ebp+12]
and	eax, [ebp+8]

pop	ebp
ret

AND_gate	ENDP

OR_gate	PROC

;-----OR_gate takes parameters a and b then it will OR the results back-----;
push	ebp
mov	ebp, esp

mov	eax, [ebp+12]
or	eax, [ebp+8]

pop	ebp
ret

OR_gate	ENDP

XOR_gate	PROC

push	ebp
mov	ebp, esp
mov	eax, [ebp+12]
xor	eax, [ebp+8]

pop	ebp
ret

XOR_gate	ENDP

full_adder	PROC

;-----Full Adder: Ai XOR Bi XOR cin-----;
;[ebp+8]	= binv
;[ebp+12]	= and_result
;[ebp+16]	= xor_result

push	ebp
mov	ebp, esp

;xor_result AND binv
;If subraction, AND gate will invert B
mov	eax, [ebp+16]	;xor_result
and	eax, [ebp+8]	;xor_result AND binv

;(xor_result AND binv) OR and_result
or	eax, [ebp+12]	;carry result

pop	ebp
ret

full_adder	ENDP

END ; end of source code