CSCI176 Midterm Review

Definitions

Instruction-level parallelism (ILP)	Improve processor performance by having multiple processors simultaneously execute instructions.
Superscalar	At run time, a processor supports multiple dynamic issues and multiple instructions.
Thread-level parallelism (TLP)	Improve processor performance by having threads to simultaneously execute instructions.
Coarse-grained	Switching to threads that are waiting for a time-consuming operation to be completed (e.g. loading from main memory).
Finer-grained	Switching threads after each instruction skipping stalled threads.
Simultaneous multithreading (SMT)	Variation of Coarse and Fine-grained.
Single instruction, multiple data (SIMD)	Perform the same instruction on multiple data. Such as having threads perform addition on an array of integers.
Multiple instruction, multiple data (MIMD)	Multiple simultaneous instructions on multiple data. Fully independent processing units each with its own ALU.
Page table	To prevent multiple programs from accessing other in-used memory blocks, they are assigned virtual memory address that are stored in a page table. The page table will translate the virtual memory into physical memory address. Thus in reality, all the memory for a program is scattered physically in the main memory.
Translation-lookaside buffer (TLB)	Like a memory cache, but it's a page cache.
Page fault	When translating the virtual memory into a physical memory and the physical memory doesn't exist, then that's a page fault.

Shared-memory vs Data passing

Shared-memory is faster. P1 writes to memory (1 clock), P2 reads from memory (1 clock).
Data passing is slower. P1 sends data to the INPUT network, Operating System handles the I/O (which is much slower and uses more clock time), then P2 will read from the INPUT.

BUS communication

Each processor is connected by a bus. Contention problem: only one instruction is allowed in the bus at one time.
Solution? Switched interconnections.

X-Bar switch

You can do processor to processor or processor to memory module communication by turning on some switches. Faster than bus system, but cost is higher.

From linear array to Ring

A ring is like an array but it loops back to the first array.
To find out the position of a node: E/W Mod #of nodes

Exclusive OR routing

Source: 010	Destination: 101

l1 (right)	l2(up or down)	l3(in or out)

010
   XOR	101
111	l3	l2	l1

take rigth most link l1

011
 XOR	101
110	l3	l2
take right most link l2

001
 XOR	101
100	l3
take link l3

101
 XOR	101
000	destination arrived

Omega Network

8 nodes then lg 8 = 3 stages
0 high, 1 low
Problem is there're only one path to the destination node. If that path is broken, then communication error will happen.

Benes Network will fix that problems